## Slide 1: Optimization of O3 Monitor NAAQS Compliance Networks
OTC/MANE-VU Spring Meeting
Hotel Palomar Philadelphia
117 South 17th Street
Philadelphia, PA 19103
June 3, 2016
Will Ollison (American Petroleum Institute)

## Slide 2: Different O3 FEMs Report Different DVs
Different photometer O3 scrubber designs have different local interference effects - Spicer et al. 2010 JAWMA 60:1353-1364.
Different photometer O3 scrubber designs have different local ambient humidity effects - Wilson & Birks. 2006 ES&T 40: 6361-6367.
Different allowed 2-15 meter inlet heights report different near-ground O3 gradient levels - 2006 O3 Criteria Document. Section 3.3.1, pp. 3-15 to 3-17.

## Slide 3: Monitor Number Distribution 2014 O3 Compliance Network
NAAQS Docket EPA-HQ-OAR-2008-0699
Chart: 
| 2B 202/205 | Dasibi 1003/8 | ECOTECH 10 | Horiba 360/70 | ML 8810 | TAPI 400E, T400 | TAPI T265 | Teledyne ML9810-1010 | Thermo 49, 49C, 49i
Monitor Number Distribution 2014 O3 Compliance Network | 4 | 23 | 3 | 8 | 1 | 630 | 2 | 9 | 620

## Slide 4: EPA Earlier Condoned Positive Monitor Bias as Protective
“…it has been our recommendation to either accept the possibility of some error in the UV ozone measurements (such error being conservative in regard to protection of human health), or (particularly at sites having exposure to nearby sources of aromatic hydrocarbon pollutants) eschew UV ozone monitors in favor of [ethylene] chemiluminescence monitors. Some argument could be made for a correction to chemiluminescence ozone measurement data for water vapor based on the positive interference relationship observed. However, again we have long recommended against correction for the following reasons: 1) the error is only a few percent under most conditions [2015 ASTM D5149 – errors up to +12%] , 2) the error is conservative with respect to protection of human health, 3) concurrent measurement of water vapor concentration at each ozone site is costly in terms of the additional equipment, labor, and QC required, and 4) correcting data introduces opportunity for additional errors that could be worse than the original error…”
G.J. Foley May 6, 1991 Memo to Region 1; ASTM D5149 O3 Ethylene Chemiluminescence Method, Table A2, October 2015.

## Slide 5: EPA Now Urges Compliance Network Optimization
EPA’s revised monitor upgrading guidance is laudable:
“…If a monitoring agency suspects that an analyzer is susceptible to potential measurement interferences due to its location, the agency can temporarily collocate that analyzer with a FEM NO-CL [chemiluminescence] ozone analyzer…to determine if interferences exist. If the monitoring agency determines interferences are an issue…they can replace that analyzer with a NO-CL analyzer or another FEM with a scrubber that is not susceptible to the interferences present…”
R. A. Wayland August 20, 2015 Memo to W. M. Ollison.

## Slide 6: Only Area DV Monitors Need Local Optimization
O3 design values (DVs) typically occur on hot, humid, stagnant days which maximize local interferences, humidity effects, and vertical O3 monitor gradients.
O3 NAAQS are now effectively 99th centile extreme value standards for 12-month smog seasons but compliance is still determined from only the single highest monitor DV in the compliance area.
Thus only a few local DV sites can be economically upgraded to verify a compliance network’s accuracy.

## Slide 7: Recommendations
NAAQS compliance would benefit by reducing the positive interference bias of relatively few potential design value network sites with interference-free FEMs (TAPI T265 NO-CL or 2B NO-GPT 211).
Lowering local DV site network inlets to 2 meters would further improve O3 NAAQS compliance until sufficient O3 gradient data is acquired to adjust DVs to 2 meter levels better matching outdoor nose heights.
Ongoing and planned EPA near-ground O3 gradient studies may acquire such DV adjustment data soon.